## Slide 1: Real-time Identification and Prediction of Danger Zones in Extreme Events
March 30, 2020

## Slide 2: Motivation
Smoke plume from chemical fire at Deer Park

## Slide 3: What happens after the event?
National Research Council 2003. Tracking and Predicting the Atmospheric Dispersion of Hazardous Material Releases: Implications for Homeland Security. Washington, DC: The National Academies Press.
Hazardous release
Quickly spreads (~Kilometers in few minutes)
Immediate first response : 0-2 Hours

## Slide 4: Area survey using drone networks
Quick
Reliable
Generalizable
Easy to deploy
Discussion of previous work after problem formulation.

## Slide 5
System Description
GCS
Gas Sensing Drone
Initialize from GCS
Equipped with Gas Sensors
Gas Sensors are point sensors.
Spatial Range
Contains Plume
Average wind speed is also known.
Source location in Known.
Plume
Plume : conc. > Safe threshold conc.
Single Emission Source
Moving
time | loc | Conc.
t1 | u1 | c1
t1 | u2 | c2
t2 | u3 | c3
Notes: Why not camera?
Talk about sources: fire, accident, industrial emission

## Slide 6: Representation of Plume
Snapshot at some time t
Discretized Snapshot at some time t : 2D Matrix
State of the system at time ‘t’

## Slide 7: Problem Statement
 | 1 | 2 | … | n
End Goal
For each time window, Identify unsafe regions and Predict regions at risk in future.

## Slide 8: Problem Statement
 | 1 | 2 | … | n
Goal
For each time window, Identify unsafe regions and Predict regions at risk in future.
Objectives
For each given set of initial measurements:
1- Estimate the state of system (Gas Distribution Map (GDM)) for current time such that :
2- Predict the state for next time window such that :
For each given set of initial measurements:
1- Estimate the state of system (Gas Distribution Map (GDM)) for current time such that :
𝑳_𝟏=(𝐦𝐢𝐧)┬(𝒄_𝒆 [𝒏])⁡ ‖ 𝒄_𝒆 [𝒏]−𝒄_𝒕𝒓𝒖𝒆 [𝒏] ├ ┤‖_𝟐 ┤
2- Predict the state for next time window such that :
𝑳_𝟐= (𝐦𝐢𝐧)┬(𝒄_𝒑 [𝒏])⁡ ‖ 𝒄_𝒑 [𝒏+𝟏]−𝒄_𝒕𝒓𝒖𝒆 [𝒏+𝟏] ├ ┤‖_𝟐 ┤
Choose next sampling locations based on error between predictions and actual measurements.
Objectives
Choose next sampling locations based on error between predictions and actual measurements.
Focus of today’s presentation
Reliability + Generalizability
Quick
Notes: Decoupling Space and Time

## Slide 9: Problem Statement
 | 1 | 2 | … | n
Goal
For each time window, Identify unsafe regions and Predict regions at risk in future.
Objectives
For each given set of measurements and previous predictions :
Estimate the Gas Distribution Map (GDM) for current time such that :
Predict the GDM for next time step such that :
For each given set of measurements and previous predictions :
Estimate the Gas Distribution Map (GDM) for current time such that :
𝑳_𝟏=(𝐦𝐢𝐧)_(𝒄_𝒆 [𝒏])⁡ ‖ 𝒄_𝒆 [𝒏]−𝒄_𝒕𝒓𝒖𝒆 [𝒏] ├ ┤‖_𝟐 ┤
Predict the GDM for next time step such that :
𝑳_𝟐= (𝐦𝐢𝐧)┬(𝒄_𝒑 [𝒏])⁡ ‖ 𝒄_𝒑 [𝒏+𝟏]−𝒄_𝒕𝒓𝒖𝒆 [𝒏+𝟏] ├ ┤‖_𝟐 ┤
Choose next sampling locations that based on error between predictions and actual measurements.
Objectives
Choose next sampling locations that based on error between predictions and actual measurements.
Constraints
1- Drone Flight Time
2- Drone Speed
3- Sensor Response Time
Strictly limited amount of measurements
Notes: Decoupling Space and Time

## Slide 10: State Space System Representation
Transition Model
Measurement Model
Transition Matrix nxn
Input/Source
Process noise/uncertainty about A
Indicator Matrix
mxn
Measurement noise

## Slide 11: Framework
Initialization
Flight planning
Design
Given and estimate c[n]
Predict c[n+1] =A*c[n]
Information about transition matrix
for prediction
Decoupling Space and Time extrapolation

## Slide 12: System Identification : Learning A
Purely Data Driven Approach
Data+ Domain Knowledge Approach
Time-stamped conc. measurements
Source location, Average wind velocity

## Slide 13: Purely Data-Driven System Identification
Matrix-Pencil Method
  Constructs dynamical systems based on time-series data
  Computationally cheap.
  Commonly used for reduced order system-models
Construct shifted Hankel matrices
Take SVD of
Estimate A
[1] : Ionita A.C. and Antoulas A.C., Matrix pencils in time and frequency domain system identification, in Developments in Control Theory, towards Glocal Controlº, edited by Qiu L., Chen J., Iwasaki T., and Fujioka H., IET Control Engineering Series, vol. 76, pages 79±88 (2012).

## Slide 14: Domain Knowledge : Physical Model
Wind
Source
The emission from source is transported in the space by
1- Diffusion
2- Advection
How can we express this transport phenomenon mathematically?
Convection-Diffusion Partial Differential Equation
Notes: Source of a heat, gas, chemical

## Slide 15: Transport Equation
Change in concentration due to diffusion
Convective flux :Transported by wind
Source term
Closed form solution do not exist.
Numerical Solution  Discretize in Space and time
  Instantaneous source
Where
Notes: Talk about INSTANTANEOUS SOURCE

## Slide 16: Discretized Transport Equation
Mass matrix (comes from numerical scheme)
{0,2/3,1}
From time integration scheme
Convection field
Diffusion field
Diffusivity coefficient
Given that wind magnitude and diffusivity coefficient are constant in space.
A

## Slide 17: Putting everything together
1- Initialize and collect some data
2- Estimate A:
3- Estimation Step :
Update transition matrix .
4- Prediction Step :
5- Repeat 3-4 ‘K’ times.
6- Design (In progress)
prediction
correction
Kalman gain provides optimum way to combine prediction with error assuming Gaussian process noise.

## Slide 18: Previous Work
 | Reliability | Generalizability | Quick & Easy to deploy
Simplified model obtained from ideal assumptions |  |  | 
Extremely complex Models that require geographical & weather data |  |  | 
Steady state Plume (conc. fixed over time) |  |  | 
Source Localization |  |  | 
Very few works incorporate drone constraints with a time-varying plume and design an end-to-end system and evaluate over field experiment.

## Slide 19: Evaluate performance of purely Data-driven method(1) and Model-based method(2) with experimental data

## Slide 20: Experimental Data
Thorny Island Dataset (1982-84)
Instantaneous gas source
Different group of sensors recorded data for different trials
Per second conc. Data recorded

## Slide 21: Part 1: Evaluate Prediction Accuracy
Do not extrapolate sensor data (40-50 positions) in space. Evaluation performed at true values only.
Use all measured values at one time instance to predict the next.
Performance metric :
  %False Negative
  %False Positive
  Log Error Norm[1]
  Still looking for better metric
[1] : Schmehl, Kerrie J., Sue Ellen Haupt, and Michael J. Pavolonis. "A genetic algorithm variational approach to data assimilation and application to volcanic emissions." Pure and applied geophysics 169.3 (2012): 519-537.

## Slide 22: Results
Mean % Error over the time window
Note that purely data-driven has an addition offset of first 50—60 samples needed to construct Hankel Matrix.
Trial 1
Trial 2
Trial 3
Data-Driven
Model-based

## Slide 23: Results
Trial 1 Trial 2 Trial 3
Trial 1 Trial 2 Trial 3
Data-Driven
Model-based

## Slide 24: Explanation
The data-driven method doesn’t anticipate the impact generated by one sensor on the other in future.
The model-based exploits spatial connectivity while extrapolating in time.

## Slide 25: Future Objectives
Design the feedback loop to adaptively sample using drone.
Evaluate the performance over different initializations.
Revisit Spatial Extrapolation/State estimation.